## Slide 1
AUTOMOTIVE ELECTRICAL
Ohm's Law
Voltage, current, resistance, and power - organized for calculation, measurement, and diagnosis.
STUDENT VERSION
V = I x R | P = V x I
OHM'S LAW
01
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 2
CORE RELATIONSHIP
One small circuit connects all four quantities
CORE RELATIONSHIP
02
1 V
across
1 ohm
produces
1 A
and
1 W
V = I x R
P = V x I
Voltage drives current through resistance.
Voltage and current determine power.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 3
LEARNING OUTCOMES
By the end, you should be able to...
LEARNING OUTCOMES
03
01
Explain
Describe how voltage, current, resistance, and power affect one another.
02
Calculate
Use two known values to solve for the missing circuit value.
03
Measure & Diagnose
Connect a digital multimeter correctly and compare actual values to expected values.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 4
FOUNDATIONS
Four quantities describe circuit behavior
FOUNDATIONS
04
V
Voltage
Electrical potential difference - often compared to pressure.
Unit: volt (V)
I
Current
Rate of electrical charge flow.
Unit: ampere (A)
R
Resistance
Opposition to current flow.
Unit: ohm (Ω)
P
Power
Rate of electrical energy transfer.
Unit: watt (W)
Note: Some automotive diagrams use E for voltage and A for current.
ohm symbol = Ω
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 5
OHM'S LAW
If you know two values, you can calculate the third
OHM'S LAW
05
V
I
R
Solve voltage
V = I x R
Current multiplied by resistance
Solve current
I = V / R
Voltage divided by resistance
Solve resistance
R = V / I
Voltage divided by current
Cover the unknown letter in the triangle. The remaining letters show the operation.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 6
WATT'S LAW
Power is the product of voltage and current
WATT'S LAW
06
P
I
V
Solve power
P = V x I
Voltage multiplied by current
Solve voltage
V = P / I
Power divided by current
Solve current
I = P / V
Power divided by voltage
A 12 V load drawing 2 A consumes 24 W.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 7
CAUSE & EFFECT
Voltage and resistance control current
CAUSE & EFFECT
07
Baseline
1 V
/
1 Ω
=
1 A
Reference point
Voltage doubles
2 V
/
1 Ω
=
2 A
Current doubles
Resistance doubles
1 V
/
2 Ω
=
0.5 A
Current is cut in half
Resistance halves
1 V
/
0.5 Ω
=
2 A
Current doubles
CAUSE & EFFECT
07
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 8
TECHNICIAN APPLICATIONS
Ohm's Law turns measurements into decisions
TECHNICIAN APPLICATIONS
08
01
Predict a value
Calculate expected current, resistance, or voltage drop before connecting the circuit.
02
Diagnose a fault
Compare expected values with meter readings to locate opens, shorts, or unwanted resistance.
03
Size a component
Choose the correct resistor, fuse, wire gauge, or power rating for the job.
Example: Use V = I x R to select an LED current-limiting resistor.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 9
STUDENT PRACTICE
Choose the formula before substituting numbers
STUDENT PRACTICE
09
01
A circuit draws 4 A through a 3 ohm load. Find voltage.
Use V = I x R
Answer: __________ V
02
A 12 V source is connected to a 3 ohm load. Find current.
Use I = V / R
Answer: __________ A
03
A 12 V circuit draws 4 A. Find total resistance.
Use R = V / I
Answer: __________ ohms
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 10
CIRCUIT MEASUREMENTS
Use consistent labels for totals and individual loads
CIRCUIT MEASUREMENTS
10
WHOLE CIRCUIT
Vt
Source voltage
Available voltage across the entire circuit
It
Total current
Current supplied to the entire circuit
Rt
Total resistance
Equivalent resistance seen by the source
Pt
Total power
Power consumed by the entire circuit
INDIVIDUAL LOAD
R1, R2
Resistance of load 1, load 2, and so on
VR1, VR2
Voltage drop across each load
IR1, IR2
Current through each load or branch
PR1, PR2
Power consumed by each load
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 11
CIRCUIT MEASUREMENTS
Read the circuit before touching the meter
CIRCUIT MEASUREMENTS
11
LABEL CHECK
Vt
Source voltage
Rt
Total resistance
It
Total current
VR1 / VR2
Load voltage drops
R1 / R2
Load resistances
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 12
CIRCUIT MEASUREMENTS
A repeatable process prevents meter mistakes
CIRCUIT MEASUREMENTS
12
01
Identify
What value are you looking for?
02
Select
Choose the correct meter mode and range.
03
Prepare
De-energize or energize as required.
04
Connect
Place the meter in parallel or series correctly.
05
Compare
Compare actual readings with calculated values.
Meter setup is part of the diagnosis - not a separate step.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 13
CIRCUIT MEASUREMENTS
Measure source voltage across the power supply
CIRCUIT MEASUREMENTS
13
Vt - TOTAL VOLTAGE
1. Set the meter to DC volts.
2. Place the red lead on source positive and the black lead on source negative.
3. Record the available voltage before testing the rest of the circuit.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 14
CIRCUIT MEASUREMENTS
Measure voltage drop across a powered load
CIRCUIT MEASUREMENTS
14
VR1 - VOLTAGE DROP OF LOAD 1
1. Keep the circuit energized and operating.
2. Place one lead on each side of the load.
3. The reading shows how much electrical potential is dropped across that load.
Voltage is not "used up"; energy is transferred as voltage drops across loads.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 15
CIRCUIT MEASUREMENTS
Resistance requires a de-energized circuit
CIRCUIT MEASUREMENTS
15
STOP: Remove power before connecting an ohmmeter.
Isolate the component
Disconnect at least one side so other circuit paths do not change the reading.
Discharge stored energy
Capacitors and powered modules can damage the meter or create a false reading.
Check the meter leads
Short the leads together first; the reading should be near 0 ohms.
Consider temperature
Metallic conductors usually gain resistance as temperature rises.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 16
CIRCUIT MEASUREMENTS
Isolate the load before measuring R1
CIRCUIT MEASUREMENTS
16
LOAD RESISTANCE
1. Remove circuit power.
2. Disconnect at least one load terminal.
3. Set the meter to ohms.
4. Place one lead on each side of the load.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 17
CIRCUIT MEASUREMENTS
Measure total resistance across the circuit
CIRCUIT MEASUREMENTS
17
TOTAL RESISTANCE - Rt
1. Disconnect the circuit from the source.
2. Keep the intended circuit path complete.
3. Measure from the source-positive connection to the source-negative connection.
The reading is the equivalent resistance the source will see.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 18
CIRCUIT MEASUREMENTS
An ammeter must become part of the circuit path
CIRCUIT MEASUREMENTS
18
TOTAL CURRENT - It
1. Move the red lead to the correct current jack.
2. Open the circuit and connect the meter in series.
3. Start on the highest safe range.
4. Energize the circuit and read current.
Never place an ammeter directly across a voltage source.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 19
02
Watt's Law
Use voltage and current to calculate electrical power.
WATT'S LAW
19
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 20
WATT'S LAW
Power is the rate of energy transfer
WATT'S LAW
20
P = V x I
12 V x 2 A = 24 W
If voltage stays constant, more current means more power. If current stays constant, more voltage means more power.
Load rating
Bulbs, motors, heaters, and modules are rated in watts.
Heat
Higher power usually means more heat that wiring and components must handle.
Diagnosis
Unexpected power can reveal excessive current draw or low available voltage.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 21
STUDENT PRACTICE
Apply Watt's Law
STUDENT PRACTICE
21
01
A 12 V lamp draws 3 A. Find power.
Use P = V x I
Answer: __________ W
02
A 60 W load operates at 12 V. Find current.
Use I = P / V
Answer: __________ A
03
A 24 W load draws 2 A. Find voltage.
Use V = P / I
Answer: __________ V
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 22
03
Series Circuits
One current path. Voltage divides. Resistance adds.
SERIES CIRCUITS
22
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 23
SERIES CIRCUITS
A series circuit has one path from positive to negative
SERIES CIRCUITS
23
One path
The same current passes through every load in sequence.
One open stops all loads
A break anywhere interrupts current through the entire circuit.
Voltage divides
Each load drops part of the source voltage.
Current stays the same
The same current flows through every series component.
More series resistance means less total current.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 24
SERIES CIRCUITS
Four laws solve every basic series circuit
SERIES CIRCUITS
24
Voltage
Vt = VR1 + VR2 + ...
All voltage drops equal source voltage
Current
It = IR1 = IR2 = ...
Current is the same everywhere
Resistance
Rt = R1 + R2 + ...
All resistances add together
Power
Pt = PR1 + PR2 + ...
All load power adds together
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 25
SERIES CIRCUITS
Each load has its own voltage drop and resistance
SERIES CIRCUITS
25
Vt
Source voltage
R1 / R2
Individual load resistance
VR1 / VR2
Voltage drop across each load
It
Same current through both loads
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 26
SERIES CIRCUITS
Series voltage drops add back to source voltage
SERIES CIRCUITS
26
KIRCHHOFF'S VOLTAGE LAW
Vt = VR1 + VR2
12 V = 6 V + 6 V
The load with the greatest resistance receives the greatest voltage drop.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 27
SERIES CIRCUITS
Total resistance is the sum of every series load
SERIES CIRCUITS
27
Rt = R1 + R2 + ...
2 ohms
+
2 ohms
=
4 ohms
Adding a series load always increases total resistance and reduces current when source voltage stays constant.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 28
SERIES CIRCUITS
Current is the same at every point in a series circuit
SERIES CIRCUITS
28
It = IR1 = IR2
0.480 A = 0.480 A = 0.480 A
An ammeter placed anywhere in the single current path should show the same reading.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 29
WORKED EXAMPLE
Solve the series circuit one relationship at a time
WORKED EXAMPLE
29
Given: Vt = 12 V R1 = 2 ohms R2 = 4 ohms
1
Find Rt
2 + 4 = 6 ohms
2
Find It
12 / 6 = 2 A
3
Find VR1
2 A x 2 ohms = 4 V
4
Find VR2
2 A x 4 ohms = 8 V
5
Verify
4 V + 8 V = 12 V
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 30
STUDENT PRACTICE
Series circuit problems
STUDENT PRACTICE
30
01
Find Vt: It = 2 A, R1 = 3 ohms, VR2 = 12 V
Answer: ____________________
02
Find Vt: R1 = 3 ohms, R2 = 2 ohms, VR2 = 4 V
Answer: ____________________
03
Find VR1: It = 2 A, R1 = 3 ohms
Answer: ____________________
04
Find VR1: It = 2 A, R2 = 4 ohms, Vt = 14 V
Answer: ____________________
05
Find Rt: Vt = 14 V, R1 = 3 ohms, It = 2 A
Answer: ____________________
06
Find Rt: R1 = 3 ohms, VR2 = 4 V, It = 2 A
Answer: ____________________
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 31
04
Parallel Circuits
Multiple current paths. Equal branch voltage. Current adds.
PARALLEL CIRCUITS
31
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 32
PARALLEL CIRCUITS
Parallel branches share the same two nodes
PARALLEL CIRCUITS
32
Multiple paths
Current can travel through more than one branch from positive to negative.
Equal branch voltage
Each branch has the full source voltage across it.
Current divides and recombines
Total current equals the sum of all branch currents.
Resistance decreases
Adding a branch lowers equivalent resistance and increases total current.
One failed branch does not stop current through the remaining branches.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 33
COMPARE
Series and parallel circuits follow different rules
COMPARE
33
Feature | Series | Parallel
Current paths | One | Two or more
Current | Same everywhere | Splits among branches
Voltage | Divides across loads | Full source voltage across each branch
Resistance | Adds together | Lower than the smallest branch
Single open | Stops the entire circuit | Only stops the affected branch
Common use | Simple chains and sensors | Automotive lighting and accessories
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 34
PARALLEL CIRCUITS
Every branch receives the full source voltage
PARALLEL CIRCUITS
34
Vt = VR1 = VR2
12 V = 12 V = 12 V
Treat each branch like its own circuit connected directly across the source.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 35
PARALLEL CIRCUITS
Branch resistance determines branch current
PARALLEL CIRCUITS
35
IR = VR / R
12 V / 12 ohms = 1 A
12 V / 6 ohms = 2 A
The lower-resistance branch carries more current.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 36
PARALLEL CIRCUITS
Total current is the sum of all branch currents
PARALLEL CIRCUITS
36
It = IR1 + IR2 + IR3
1 A + 2 A + 6 A = 9 A
The total current leaves the source, divides among the branches, and recombines before returning.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 37
PARALLEL CIRCUITS
Parallel Rt is lower than the smallest branch
PARALLEL CIRCUITS
37
Rt < smallest branch resistance
01
Equal branches
Rt = branch R / number of branches
02
Two unequal branches
Rt = (R1 x R2) / (R1 + R2)
03
Any number of branches
Rt = 1 / (1/R1 + 1/R2 + ...)
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 38
PARALLEL RESISTANCE
Equal branches use the fastest resistance shortcut
PARALLEL RESISTANCE
38
Simple equal branches
4 ohms / 2 branches = 2 ohms
Equal branches with series loads
6 ohms / 2 branches = 3 ohms
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 39
PARALLEL RESISTANCE
Two unequal branches use product over sum
PARALLEL RESISTANCE
39
Rt = (R1 x R2) / (R1 + R2)
Example: 2 ohms in parallel with 4 ohms
Rt = (2 x 4) / (2 + 4) = 8 / 6 = 1.33 ohms
Quick check: 1.33 ohms is less than the smallest branch, 2 ohms.
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 40
PARALLEL RESISTANCE
Use reciprocals for any branch count
PARALLEL RESISTANCE
40
Rt = 1 / (1/R1 + 1/R2 + 1/R3)
Example: 4 ohms, 6 ohms, and 12 ohms
1/Rt = 1/4 + 1/6 + 1/12
1/Rt = 0.25 + 0.167 + 0.083
1/Rt = 0.50
Rt = 2 ohms
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 41
WORKED EXAMPLE
Find total current in two equal parallel branches
WORKED EXAMPLE
41
METHOD 1 - TOTAL RESISTANCE
Rt = 4 ohms / 2 branches = 2 ohms
It = 12 V / 2 ohms = 6 A
METHOD 2 - BRANCH CURRENT
IR1 = 12 V / 4 ohms = 3 A
IR2 = 12 V / 4 ohms = 3 A
It = 3 A + 3 A = 6 A
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 42
WORKED EXAMPLE
Use total current to solve for an unknown branch
WORKED EXAMPLE
42
Given: Vt = 12 V, It = 4 A, R1 = 6 ohms
1
Find IR1
12 V / 6 ohms = 2 A
2
Find IR2
4 A - 2 A = 2 A
3
Find R2
12 V / 2 A = 6 ohms
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 43
STUDENT PRACTICE
Parallel circuit problems
STUDENT PRACTICE
43
01
Two 12 ohm branches are connected to 12 V. Find Rt and It.
Equal branches, then I = V / R
Answer: __________ Rt / It
02
A 6 ohm branch and a 3 ohm branch share 12 V. Find both branch currents and It.
IR = V / R; currents add
Answer: __________ A
03
Three branches are 4, 6, and 12 ohms. Find Rt and It at 12 V.
Use the reciprocal formula
Answer: __________ Rt / It
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 44
REFERENCE
Circuit formula sheet
REFERENCE
44
Find | Basic formula | Series rule | Parallel rule
Voltage | V = I x R | Vt = VR1 + VR2 + ... | Vt = VR1 = VR2 = ...
Current | I = V / R | It = IR1 = IR2 = ... | It = IR1 + IR2 + ...
Resistance | R = V / I | Rt = R1 + R2 + ... | Rt < smallest branch
Power | P = V x I | Pt = PR1 + PR2 + ... | Pt = PR1 + PR2 + ...
Equal parallel R | - | - | Rt = branch R / branches
Two parallel R | - | - | Rt = R1 x R2 / (R1 + R2)
Any parallel R | - | - | Rt = 1 / (1/R1 + 1/R2 + ...)
Verification | Use units | Sum of drops = source | Sum of branch I = total I
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]

## Slide 45
EXIT TICKET
Show what you know
1. A 12 V circuit has 4 ohms of resistance. What is current?
2. What must happen to current if resistance increases and voltage stays constant?
3. Name one rule that is different in series and parallel circuits.
4. Which meter measurement requires the meter to be connected in series?
Explain one answer in your own words.
EXIT TICKET
45
Notes: [Sources]
- User-provided source: EL - 05.1 Ohm's Law (Student Version).pdf
[/Sources]